## Slide 1: STEREO Spacecraft and Ground Segments Status
January 18, 2022
Owen Dudley
STEREO Mission Operations Manager
(240) 228-4568

## Slide 2: STEREO Phase E Organization Chart
Project
Scientist
T. Kucera
Mission Director
J. Dickey
Mission System Engineer
J. Halverson
FDF
Project
Manager
D. Grant
Mission
Operations
O. Dudley
System
Engineering
D. Wilson
DSN
Technical
SSC
W. Thompson
Science
Teams
DSN
Scheduling
Payload
Operations
Teams
GSFC
APL
JPL
NRL, UCBerkeley, UNH, UMinn
Mission
Operation
Team
Subsystem
Lead
Engineers
Changes in red

## Slide 3: MOC Status
Mission operations continues to collect ~5 Gbits per day in support of the science mission.
Downlink rates: Varies, 720 kbps to 360 kbps depends on antenna size and track elevation
  Baseline downlink to increase to 720 kbps in Spring 2022
Since 2012, using the 3 ESA deep space stations (35 meter) when needed to maintain data return and in-situ science data continuity
  Due to high periodic DSN loading
Total manpower is approximately 2.9 SM/M for Spacecraft Controllers
MOC Unix workstations are being refreshed (Intel x86 architecture)
  IONET Command & Control workstations completed in 2019.
    Included upgrading to CCSDS SLE Bluebook version 4
  Majority of the DMZ Planning/Assessment workstations completed in 2021.
    The last four servers will be completed in 2022
Special Observatory Events
  SECCHI COR2 Deep Exposure Campaign for each Parker Solar Probe perihelion
  SECCHI stepped calibrations rolls (~every 3 months)
  142 Momentum Dumps to date on STEREO-A (~every 5-6 weeks)

## Slide 4: Spacecraft Status
STEREO-A operating nominally using no gyro operations
  No gyro operations limits IMU use to fault protection and high value science events (project scientist directed)
  IMU status (gyros)
    IMU-A – failed in April 2007
    IMU-B – limited remaining life (estimated at ~1400 hours)
Last Spacecraft Assessment Review was Oct 2020; next review on Feb 17, 2022
  Brief intermittent losses of fine pointing
    12 occurrences (since post solar conjunction in July of 2015) of low wheel speeds (one or more wheels running for a prolonged period at or near the zero speed avoidance threshold)
      Last occurrence was 2018-292
      Probable cause is bearing lubricant distribution problem after wheel stopped
      Operating with 4 wheels; can tolerate failure of one
      Wheels rated for 15 year lifetime; no evidence yet of pending failure
  Power, Thermal, Comms, Avionics, Flight Software – all solid
Current (11/24/2021) usable propellant load, measured by PVT, is:
  38.43 ± 0.46 kg (vs. 40.84 ± 0.44 kg @ 2016.06.15)
  Burn Rate of ~0.3 kg/year equals ample supply remaining for operations.