| IMPACT UCB LVPS/HVPS Review CLOSURE STATUS (8/9/02) |
| --- |
| Action No. | Action Item TITLE | ORIGINATOR | STATUS | DATE CLOSED |
| 1 | HVPS Temperature test | Brian King | To be done |  |
| 2 | SIT HVPS Grounding | Shane Hynes | To be defined |  |
| 3 | Potting material | Harry Culver | Done |  |
| 4 | Capacitive load testing | Harry Culver | Plastic only |  |
| 5 | LVPS Soft Start | Shane Hynes | To be done |  |
| 6 | LVPS Input Voltage Testing | Harry Culver | To be done |  |
| 7 | Oscillation Protection | Harry Culver | Done |  |
| 8 | Loss of synchronization circuitry | Harry Culver | Breadboard tested |  |
| 9 | Survival of 40V | Harry Culver | Done |  |
| 10 | IDPU LVPS Clarity | Harry Culver | Done |  |
| 11 | Add grounding jumpers | Harry Culver | To be done |  |
| 12 | Terminate shields | Harry Culver | In layout |  |
| 13 | Add capacitor | Harry Culver | To be done |  |
| 14 | PLASTIC ripple requirements | Shane Hynes | Received |  |
| 15 | Grounding requirement for PLASTIC LVPS | Ken Crocker | To be done |  |

|  | Action Item | Number: 1 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Brian King | Phone: | TBD | Organization: | UNH |
| Category: | HVPS |
| Title: | HVPS Temperature test |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | IMPACT should do temperature test of ETU HVPS to expected temperatures. |
| Supporting Rationale: |  |
| Response: | Impact will temperature test hvps etu per spec. A brief hot air gun test showed no issues, but a more formal test will be performed now that unit is potted. |

|  | Action Item | Number: 2 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Shane Hynes | Phone: | 301-286-1016 | Organization: | GSFC/460 |
| Category: | HVPS |
| Title: | SIT HVPS Grounding |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify that SIT is using its ground from the HVPS in accordance with the EMI/EMC requirements document, with respect to GND and Chassis. |
| Supporting Rationale: |  |
| Response: |  |

|  | Action Item | Number: 3 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | Materials |
| Title: | Potting material |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify potting material is on the materials list submitted to the materials branch at GSFC. |
| Supporting Rationale: |  |
| Project Response: | The following are the materials used in the low and high voltage assemblies HV vacuum pot is with Cytec Conothane EN-11 B and EN-4A The securing epoxy is Scotch weld 1838 The transformer potting is Scotchcast 280 The board coating is Vantico 5750 The stake compound is Vantico 5753 These have been added to the materials list. |

|  | Action Item | Number: 4 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Capacitive load testing |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | UCB to get the capacitive load values for all LVPS loads and use these values in the testing of the LVPS. |
| Supporting Rationale: |  |
| Project Response: | Capacitive Loads have been included in LVPS Requirements document. Will be used in analysis, test. |

|  | Action Item | Number: 5 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Shane Hynes | Phone: | 301-286-1016 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | LVPS Soft Start |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify soft start operation meets STEREO Requirements. |
| Supporting Rationale: |  |
| Project Response: | Soft start verified by analysis; will be verified when ETUs are built |

|  | Action Item | Number: 6 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | LVPS Input Voltage Testing |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify LVPS operation when the input voltage is ramped from 0V – 40V and back down from 40V – 0V. |
| Supporting Rationale: |  |
| Project Response: | Slow ramp up and ramp down testing will be done when ETUs are built |

|  | Action Item | Number: 7 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Oscillation Protection |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Add RC Circuit at the input to the LVPS for oscillation protection. |
| Supporting Rationale: |  |
| Project Response: | Analysis showed unit is stable without RC damping |

|  | Action Item | Number: 8 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Loss of synchronization circuitry |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Modify LVPS design to allow for the failing of the synchronization circuitry without loss of the LVPS. |
| Supporting Rationale: |  |
| Project Response: | Circuit breadboarded, tested, and incorporated into layout of ETU. IC chosen was SEL tested successfully |

|  | Action Item | Number: 9 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Survival of 40V |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify that the circuit (including the zeners) will survive the required 40V. |
| Supporting Rationale: |  |
| Project Response: | The PWM chip used on the input will survive 60 volts. The zener callout has been changed to a 1N4480 which will survive 40 volts. |

|  | Action Item | Number: 10 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | IDPU LVPS Clarity |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify that the +12.8A is + going to R33 on IDPU LVPS |
| Supporting Rationale: |  |
| Project Response: | It does. |

|  | Action Item | Number: 11 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Add grounding jumpers |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Add jumper locations to chassis ground for potential secondary returns. |
| Supporting Rationale: |  |
| Project Response: | These will be added. |

|  | Action Item | Number: 12 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Terminate shields |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Terminate transformer shields with resistive load. |
| Supporting Rationale: |  |
| Project Response: | Provision for termination has been incorporated into the layout. |

|  | Action Item | Number: 13 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Harry Culver | Phone: | 301-286-5874 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | Add capacitor |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Add capacitor on –5V output on PLASTIC LVPS. |
| Supporting Rationale: |  |
| Project Response: | A filter capacitor will be added. |

|  | Action Item | Number: 14 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Shane Hynes | Phone: | 301-286-1016 | Organization: | GSFC/460 |
| Category: | LVPS |
| Title: | PLASTIC ripple requirements |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | PLASTIC to determine ripple requirement for their LVPS. |
| Supporting Rationale: |  |
| Project Response: | PLASTIC has submitted a 10 mv ripple requirement. |

|  | Action Item | Number: 15 |
| --- | --- | --- |
|  | Project: | STP |  |
|  | Spacecraft (SC/GS/LV): | STEREO |  |
|  | System/Instrument: | IMPACT |  |
|  | Review: | PDR |  |
|  | Date: | September 11-September 13, 2001 |  |
| Originator: | Ken Crocker | Phone: | 603-862-1071 | Organization: | UNH |
| Category: | LVPS |
| Title: | Grounding requirement for PLASTIC LVPS |
| Date Closed: |  |
| Residual Risk: |  |
| Action Requested: | Verify that the grounding of the PLASTIC LVPS meet STEREO/PLASTIC requirements. |
| Supporting Rationale: |  |
| Project Response: |  |