PWB, etc:

| Problem Number | Date Found | Found By | Configuration | Description | Disposition |
| --- | --- | --- | --- | --- | --- |
| DCB-PWB-001 | 2002-5-2 | Colby @ SSL | ETU Board (Rev A) | CDR05 capacitor pads are too small. For ETU use smaller non-high-rel capacitors. For flight layout, pads will need to change. | Fixed, Rev B board |
| DCB-PWB-002 | 2002-5-2 | Colby @ SSL | ETU Board (Rev A) | UT7Q512KIPC RAMs don’t fit; the board is layed out for the 32-pin part and we have the 36-pin part. | Fixed, Rev B Board |
| DCB-PWB-003 | 2002-6-4 | Gordon | ETU Board (Rev B, S/N 1) | Reset circuit is not working. Possible excessive bias current in U11A. Change R20 to 100K; will need to test with LVPS to verify time margin between VCC>4.5V and RESET going inactive. | Change Schematic/Parts list |
| DCB-PWB-004 | 2002-6-28 | Gordon | ETU Board (Rev B, S/N 1) | Summit chip address lines reversed | Cut & jump ETU, modify flight layout, correct in Schematic |
| DCB-PWB-005 | 2002-7-01 Rev. 2002-10-04 | Gordon | ETU Board (Rev B, S/N 1) | Pull-ups required on U13 pins 1 and 3 (DMAR and DMACK) | Add 499 Pull-ups at Spare Site; modify schematic/parts list |
| DCB-PWB-006 | 2002-7-01 | Gordon | ETU Board (Rev B, S/N 1) | Pull-downs for U13 inputs are not strong enough. Change value of R26, R27, R30, R31 and R32 | Replace the five 10K Resistors with 1K Resistors; modify schematic/parts list |
| DCB-PWB-007 | 2002-7-11 | Gordon | ETU Board (Rev B, S/N 1) | Pull-ups required on U13 pins 65 and 66 (MSGINT and YFINT) | Add 1K Pull-ups at Spare Site; modify schematic/parts list |
| DCB-PWB-008 | 2002-11-18 | Gordon | ETU Board (Rev B, both) | Required for Upgrade to DCB-FPGA Rev 4 Isolate HWRST from CPURST; Add jumpers for Watchdog Timer Disable and Testpoint Enable | Cut/Jump ETU; Add jumpers (WDDIS & TPENB) and 10K pull-ups at the Spare Site. Modify schematic/parts list |
| DCB-PWB-009 | 2002-11-22 | Gordon |  | Pull-ups should be present on FPGA test I/O for the flight layout | Modify schematic/parts list |
| DCB-PWB-010 | 2002-11-22 | Curtis/Gordon |  | For more noise immunity, add 0.01 Filter Capacitors near FPGA in the flight layout. | Modify schematic/parts list |
| DCB-PWB-011 | 2002-12-02 | Curtis |  | For more margin, increase the PowerOn Reset Time Constant for the flight layout, also switch to 6.8uF tantalum surface mount. | Modify schematic/parts list |
| DCB-PWB-012 | 2003-04-25 | Curtis | ETU Board (Rev B) and Flight Board (Rev C) | RXD, an input to the processor, should be pulled-up. | Add 10K Pull-up at Spare Site; modify schematic/parts list. For Rev C DCB, refer to DCB_C_Fix1.pdf |

FPGA, etc:

| Problem Number | Date Found | Found By | Configuration | Description | Disposition |
| --- | --- | --- | --- | --- | --- |
| DCB-FPGA-001 | 2002-7-19 | Gordon | DCB-FPGA Rev 1 | Command Overflow and Command Done Interrupt Enable Bits are reversed | Fixed in DCB FPGA Rev 2 |
| DCB-FPGA-002 | 2002-7-19 | Gordon | DCB-FPGA Rev 1 | Timing Tick is not aligned with Tick1S | Fixed in DCB FPGA Rev 2 |
| DCB-FPGA-003 | 2002-7-19 | Gordon | DCB-FPGA Rev 1 | Implements CPU HOLD/HLDA with Hold Mitigation circuit – may not work with UT80C196KD in certain scenarios | Changed to “Cycle Steal” HOLD/HLDA in DCB-FPGA Rev 2 |
| DCB-FPGA-004 | 2002-7-22 | Gordon | DCB-FPGA Rev 2 | Problem with “Cycle Steal” HOLD/HLDA cycles when processor executes or reads from byte-wide memory in conjunction with DMA activity. (Processor drives upper 8 bits of data bus during byte-wide read cycles.) | Workaround: do not use byte-wide memory when DMA enabled. Fixed in DCB-FPGA Rev 3 |
| DCB-FPGA-005 | 2002-8-7 | Curtis | DCB-FPGA Rev 2 | The 1 second timing tick period is 1.049s; should be exactly 1.000s. | Fixed in DCB FPGA Rev 3 |
| DCB-FPGA-006 | 2002-8-15 | Curtis | DCB-FPGA Rev 2 and earlier | The DCB Crashes due to false edge triggering on the CPUWR signal, which causes FPGA Reset pulse and clears Page Register 0 | Fixed in DCB FPGA Rev 3 CPUWR is sampled with CLK24M rather than edge triggered (also Page Register 0 is no longer reset with FPGA Reset Pulse) |
| DCB-FPGA-007 | 2002-9-13 | Curtis/Gordon | DCB-FPGA Rev 2 and earlier | Inherent noise problems associated with all FPGA edge sensitive inputs (could be related to capacitance of debug board cable) | DCB FPGA Rev 3 samples with CLK24M (rather than uses edge triggers) CPUCLK, ALE, YFINT and MSGINT |
| DCB-FPGA-008 | 2002-10-07 | Curtis | DCB-FPGA Rev 3 and earlier | For greater overall system reliability, the FPGA should be the source of the watchdog reset. | DCB FPGA Rev 4, isolates CPU reset and adds FPGA based watchdog timer (DCB-ETU board rework , see DCB-PCB-008, required to isolate CPU Reset and implement watchdog disable) |
| DCB-FPGA-009 | 2002-11-14 | Curtis/Gordon | DCB-FPGA Rev 3 and earlier | For greater overall noise immunity, unused outputs are driven low, TestPoint Disable added. | DCB FPGA Rev 4, drives all unused outputs low (DCB-ETU board rework, see DCB-PCB-008, required to implement testpoint disable jumper) |

UP, etc.:

| Problem Number | Date Found | Found By | Configuration | Description | Disposition |
| --- | --- | --- | --- | --- | --- |
| DCB-UP-001 | 2002-6-21 | Gordon | ETU Board (Rev B, S/N 1) | Interaction between DMA and INST line causes wrong instruction fetch. Worse than errata problem. Fixed by KDS part? | Preliminary - Appears to be fixed with Rev. KDS part |
| DCB-UP-002 | 2002-9-12 | Gordon | ETU Board (Rev B, S/N 2) | Interaction between Byte configured memory and INST line. Erroneous value on INST line occurs sometimes during “double byte” data reads. Could be present in both KD and KDS Parts. | Workaround: use Page Register 0 only when operating from byte memory. DCB Byte Wide memory includes BOOT ROM & Debug board ROM/RAM. |