STEREO IMPACT FM2 SWEA Actel Replacement Instructions

The FM2 SWEA Actel (on the DAC board) was determined to be faulty by diagnostic test.  The Actel needs to be replaced.

Remove the Actel on the SWEA FM2 DAC board.  Keep the part for failure analysis.

COMPLETED BY ________________________	DATE _________________________________

Install a new Actel at the same location.  Use an RTSX32SU-1CQ208BX109 part provided by GSFC (5962-0150806QYC), programmed with the “FlightssfRevF2_Designer7.AFM’ file at GSFC

Lot Date Code __________, Serial number ___________

COMPLETED BY ________________________	DATE _________________________________

INSPECTED  BY ________________________	DATE _________________________________

Stake the part with Uralane 5750

Mix Info______________________

Cure Info_____________________

Conformal Coat with Uralane 5753.

Mix Info______________________

Cure Info_____________________

COMPLETED BY ________________________	DATE _________________________________

Approved by: _______________________________	Date: ____________________