STEREO IMPACT SWEA FM1 Test Pulser Capacitor Replacement

The FM1 SWEA Test Pulser circuit failed after Observatory level thermal vac.  Analysis shows C49 is too large and is truncating the test pulser signal.  Replace with a lower capacitance part (change from 1000pF to 100pF).  Keep removed part to verify its value.  New part from STEREO flight spares:

CDR32BP101BFUS

Manufacturer and LDC of replacement part	__________________

COMPLETED BY ________________________	DATE _________________________________

Approved by: _______________________________	Date: ____________________