STEREO IMPACT SWEA DAC CLOCK REWORK INSTRUCTIONS

Unit (FM1/FM2)______________

Install a 47pF capacitor from the THEMIS flight stock between pins 5 and 7 of U401 on the SWEA DAC board.

- Remove the conformal coat from leads 5 and 7 of U401

- Form the leads of the M39014/02-1333 such that the capacitor will lay on top of the package of U401, and the leads will bend down parallel with the DIP leads.  Be sure to get a good 90 degree bend to provide strain relief.  See attached picture.

Part Mfg & LDC___________________

- Solder the part to the DIP between leads 5 and 7 using a lap joint.

- Take a picture of the capacitor soldering

- Stake the capacitor to the DIP using Uralane 5753 A/B

Uralane batch & expiration________________

Mix Ratio__________________

- Take a picture of the staking.

COMPLETED BY ________________________	DATE _________________________________

Approved by: _______________________________	Date: ____________________