NAVAL RESEARCH LABORATORY

E.O. HULBURT CENTER

FOR

SPACE RESEARCH

Data Management Plan

for the

Sun Earth Connection Coronal and Heliospheric Investigation (SECCHI)

7906-PLN-9-0-0010

28 January 2008

Revision 2 draft 2

Approved By:		Date:

D. Moses, SECCHI Project Scientist

Approved By:		Date:

R. Howard, SECCHI Principal Investigator

Approved By:		Date:

R. Baugh, SECCHI Program Manager

RECORD OF CHANGES

| Revision Letter | Date | Title Or Brief Description | Entered By |
| --- | --- | --- | --- |
| 0.0 | October 8, 2002 | Draft for internal review | R. Howard; S. Plunkett; N. Rich |
| 0.1 | October 17, 2002 | Comments and additions | R. Howard; S. Plunkett |
| 0.2 | October 17, 2002 | Revisions | N. Rich |
| 0.3 | October 22, 2002 | Comments from J. Newmark | N. Rich |
| 0.4 | June 20, 2003 | Comments from Bernard Klein (clarification of data backup, POC location) | N. Rich |
| 0.4 | June 26, 2003 | Editorial and formatting revisions | M. Giery-Smith |
| 1.2 | July 24, 2003 | Version/document name issue resolved by author; formatting changes | N. Rich; M. Giery-Smith |
| 2 d 1 | June 30, 2004 | Minor changes, mostly to real-time telemetry description | N. Rich |
| 2 d 2 | January 28, 2008 | Updated to reflect current practice | N. Rich |

TABLE OF CONTENTS

Section	Title	Page

1	Introduction	1-1

1.1	Purpose and Scope of Document	1-1

2	Applicable Documents	2-1

2.1	Government Documents	2-1

2.1.1	Military Standards and Specifications	2-1

2.1.2	Other Publications	2-1

2.1.3	Project-Specific Documents	2-1

2.2	Order of Precedence	2-1

3	Data Products	3-1

3.1	Instrument Overview	3-1

3.2	Data Product Overview	3-1

3.3	Roles and Responsibilities	3-2

3.4	Data Processing	3-2

3.4.1	Data Acquisition	3-3

3.4.2	Data Processing Level	3-3

3.4.3	Data Flow and Data Product Generation	3-3

3.4.3.1	Pre-Flight	3-3

3.4.3.2	Flight Operations	3-4

3.4.3.3	Beacon Data	3-4

3.4.4	Data Calibration and Evaluation	3-4

3.4.5	Data Distribution and Accessibility	3-5

3.5	Data Volume	3-5

3.6	Labeling and Identification	3-6

3.7	Standards Used in Generating Data Products	3-6

3.7.1	FITS Standard	3-6

3.7.2	Time Standard	3-6

3.7.3	Coordinate Systems	3-6

4	Data Analysis	4-1

5	Data Processing System Development Plan	5-1

5.1	Timeline	5-1

5.2	Software Reuse Strategy	5-1

5.3	Testing	5-1

5.4	Configuration Management and Backup Plan	5-1

5.4.1	Software	5-1

5.4.2	Data	5-1

5.5	Equipment and Space Requirements	5-2

6	Acronym List	6-1

Appendix A	DEFINITION OF SECCHI Level 0.5 FITS HEADER	A-1

A.1	Overview	A-1

A.1.1	Main Header	A-1

A.1.2	SECCHI FITS Extension	A-1

A.1.3	Table Description	A-1

A.2	References	A-2

A.3	Main Header	A-3

A.3.1	Coordinate System	A-6

A.4	SECCHI FITS Extension	A-7

A.4.1	Extension Table Column (Field) Definitions	A-7

A.4.2	Keywords for FITS Extension	A-9

LIST OF FIGURES

Number	Title	Page

Figure 3-1  SECCHI Data Processing Flow	3-4

LIST OF TABLES

Number	Title	Page

Table 2-1  Non-Military Government Publications	2-1

Table 2-2  Project-Specific Documents	2-1

Table 3-1  SECCHI Data Product Formats	3-2

Table 3-2  Data Processing Level Definition	3-3

Table 3-3  SECCHI Data Volume	3-5

Table 5-1  Equipment and Space Requirements	5-2

# Introduction

## Purpose and Scope of Document

This Data Management Plan:

Contains a detailed description of data products suitable for data users.

Describes how data from the Sun Earth Connection Coronal and Heliospheric Investigation (SECCHI) instruments on the Solar TErrestrial RElations Observatory (STEREO) spacecraft are obtained, processed, archived and distributed.

Describes various team responsibilities.

Describes the development plan for the SECCHI Data Processing System (DPS).

# Applicable Documents

This section identifies documents that are referenced in this Data Management Plan or that provide information useful to understanding the SECCHI Project. The following documents of the exact issue shown form a part of this document to the extent referenced herein.

## Government Documents

### Military Standards and Specifications

No military standards or specification documents are applicable for the SECCHI Data Management Plan.

### Other Publications

Table 2-1  Non-Military Government Publications

| Number | Title |
| --- | --- |
| NOST 100-2.0, 1999/03/29 | NASA Science Office of Standards and Technology (NOST), Definition of the Flexible Image Transport System (FITS), http://archive.stsci.edu/fits/fits_standard/ |
| 2000/07/12 | Thompson, William, Coordinate Systems for Solar Image Data, 2000/07/12, http://orpheus.nascom.nasa.gov/~thompson/papers/coordinates.ps |

NASA	National Aeronautics and Space Administration

### Project-Specific Documents

Table 2-2  Project-Specific Documents

| Number | Title |
| --- | --- |
| (APL) 7381-9045a | STEREO Missions Operations Center (MOC) to Payload Operations Center (POC) and to STEREO Science Center (SSC) Interface Control Document (ICD) (MOC-POC ICD) |
|  | SECCHI Ground Data System Requirements |
|  | SolarSoft, http://www.lmsal.com/solarsoft/sswdoc/index_menu.html |
| (NRL) 7906-PLN-9-0-0006 | SECCHI Ground Data System Development Plan |
| SECCHI 7906-RPT-9-0-0020, NRL | SECCHI Ground Data System Requirements |
| NASA 460-PLAN-0039, GSFC, | STEREO Project Data Management Plan--A Solar-Terrestrial Probes Mission, http://gdms.gsfc.nasa.gov/gdms/plsql/frontdoor |
| 2000/08/18 | SECCHI Phase A Concept Study Report |
| (NRL) 7906-SPC-9-0-0003 | SECCHI Science Requirements and Instrument Performance Specification |

GSFC	Goddard Space Flight Center
NRL	U.S. Naval Research Laboratory

APL	The Johns Hopkins University Applied Physics Laboratory
LMSAL	Lockheed Martin Solar and Astrophysics Laboratory

## Order of Precedence

In the event of a conflict between the text of this plan and the reference cited herein, the text of this document takes precedence, except for STEREO documents. Nothing in this document, however, supersedes applicable laws and regulations unless a specific exemption has been obtained.

# Data Products

## Instrument Overview

SECCHI is a suite of remote sensing instruments consisting of two (2) white light coronagraphs (COR1 and COR2), an Extreme Ultraviolet (EUV) Imager (EUVI), and a Heliospheric Imager (HI). SECCHI will observe Coronal Mass Ejections (CMEs) from their birth at the sun, through the corona to their impact at earth. SECCHI includes a coordinated effort to provide magnetohydrodynamic (MHD) models and visualization tools to interpret the images that will be obtained from two (2) viewpoints and to extrapolate that imagery to in-situ and radio emission measurements obtained from other instruments on STEREO.

The SECCHI Instrument Suite consists of the (2) two optical packages, the Sun-Centered Imaging Package (SCIP) and the HI package, and an electronics package, the SECCHI Electronics Box (SEB).

The SCIP is a rigid optical bench, the function of which is to hold the EUVI, COR1, COR2 and Guide Telescope (GT) in co-alignment. The EUVI images the solar corona in four (4) wavelengths out to about 1.4 solar radii. The COR1 images the white light corona from 1.5 to 4 solar radii using an internally occulted coronagraph. The COR2 images the corona from 2 to 15 solar radii using an externally occulted coronagraph. The SCIP also contains the GT that provides fine pointing information for the spacecraft (S/C) attitude control system and for the EUVI Fine Pointing System (FPS).

All three (3) SCIP scientific telescopes have recloseable doors to protect the instruments during ground operations and during possible contamination events in flight. The EUVI contains a sector wheel to select the wavelength, a filter wheel to put in various aluminum filters of different thicknesses, and a shutter to time the exposures. The COR1 and COR2 have a rotating polarizer with 144 positions, and a shutter to time the exposure.

The HI package contains two (2) simple coronagraphic telescopes to directly view the Sun-Earth line. These two (2) telescopes are sheltered within a protective baffle structure to obtain the necessary rejection of bright objects outside the field, including the solar disk, and S/C glints. A small triangular baffle shields the HI-1 from the Earth-Moon system early in the mission, when they are large and bright. The HI telescopes do not have any shutters or filter/polarizer wheels.

All five (5) telescopes use the same type of Charge-Coupled Device (CCD): backside illuminated, 2k x 2k 13.5 micron pixel. The only difference is that the EUVI CCD has an uncoated backside rather than the anti-reflective (AR) coating that the other four (4) have. The CCDs are read out using the same camera design. A 14-bit analog-to-digital converter (ADC) converts the doubly sampled video signal at the pixel readout rate of 1 millionpixels/sec.

The SEB is a common electronics unit for both the SCIP and HI. It provides command and data handling, observation sequencing, mechanism drive, housekeeping, power distribution, heater control, camera interface, and S/C interface.

## Data Product Overview

SECCHI science data consist of 2048 x 2048-pixel images of the following types:

Emission line intensity images from EUVI at one (1) of four (4) wavelengths and through aluminum (Al) filters of varying thicknesses;

Total brightness images (B) from HI1 and HI2, and

Total brightness images (B), and polarized component images, from COR1 and COR2.

Additional calibration images will be available such as darks, calibration lamps, door-closed, etc. for each telescope.

All of the data are measurements of brightness or luminescence, in digital counts (DN). The science data product will be stored and distributed as uncalibrated, uncompressed FITS files, in which a binary data array is preceded by an ASCII header. The contents of the FITS file headers are described in detail in the SECCHI FITS Header Definition (Appendix A), and will include keywords to indicate instrument attitude and orbit information, all instrument settings associated with the image, information on all onboard and ground processing steps, and image statistics. Interactive Data Language (IDL) procedures will be available to convert the FITS image files into a calibrated data product. Calibration images, including pre-flight images taken for calibration or test purposes, will also be stored as FITS files.

The routine processing flow will produce the FITS images in addition to several other types of products. These additional products include browse images and movies for the World Wide Web (WWW), higher resolution movies for research, Carrington maps, and ancillary data (housekeeping tables and plots, attitude and orbit files). Lists of various events (such as CMEs, comets, etc) will be generated. Table 3-1 gives an overview of SECCHI data products and their formats, along with bytes per pixel to give an indication of data volume.

Table 3-1  SECCHI Data Product Formats

| Data Product | Format | Bytes/pix |
| --- | --- | --- |
| Science images (COR, EUVI) | FITS | 2 |
| Science images (HI) | FITS | 4 |
| Calibration images | FITS | 2 - 4 |
| Pre-flight images | FITS | 4 |
| Browse images | JPEG or GIF | ~ 0.1 or ~ 0.8 |
| Browse movies | MPEG or JavaMovie or animated GIF (512x512) | ~ 0.05 |
| Science movies | MVI (512x512) | 1 |
| Ancillary data | JPEG, GIF, Interactive Java Display, ASCII Text, or FITS | varied |
| CME Lists | ASCII/DBMS | varied |
| Comet Lists | ASCII/DBMS | varied |

JPEG	Joint Photographic Experts Group	GIF	Graphics Interchange Format

MVI	NRL-developed IDL movie format	MPEG	Motion Picture Exports Group

DBMS	Database Management System

## Roles and Responsibilities

Routine processing of SECCHI data will take place at the SECCHI POC and at the SECCHI Data Processing Facility (DPF). NRL is responsible for the POC and the DPF; software for Level 1 processing; providing software to the SSC for beacon data processing; and distribution of Level 0.5 data to the SSC. NRL will also provide the calibration data for the COR2 telescope, and the pre-flight calibration information for all the CCD camera subsystems.

The Co-Investigator institutions will be responsible for providing calibration data and any special algorithms for routine processing of data from their respective telescopes to NRL. The Co-Investigators will be responsible for performing detailed analyses of their respective subsystems and for submitting updated calibration data to NRL as necessary. The Co-Investigators will be in residence at the POC during special observing campaigns requiring real-time or near-real-time commanding.

NASA/GSFC is responsible for the COR1 telescope. LMSAL is responsible for the EUVI telescope and for the GT. The Rutherford Appleton Laboratory (RAL) is responsible for the HI-1 and HI-2 telescopes.

The SSC will have four (4) key functions:

(1) it will be the focal point for archiving STEREO data;

(2) it will be the processing center for the space weather beacon data;

(3) it will be the central point for science coordination between the instruments and other space-based and ground-based campaigns; and

(4) it will be the focal point for mission-related education, public outreach, and public affairs.

## Data Processing

The requirements for the SECCHI DPS are found in the SECCHI Ground Data System Requirements document (SECCHI 7906-RPT-9-0-0020).

### Data Acquisition

The JHU/APL MOC will provide socket and File Transfer Protocol (FTP) interfaces for all STEREO data. The interfaces are governed by the MOC-POC ICD (APL 7381-9045).

The SECCHI POC will connect to the MOC over a non-secure Internet socket during real-time contact with the spacecraft to receive housekeeping and science telemetry. During normal operations, only house-keeping and beacon data will be available in real-time to the POC.

Playback data may be retrieved from the MOC in the same way as the real-time data. The playback data are available at the MOC beginning approximately three (3) hours after reception by the MOC until 30 days after reception. The MOC also will prepare a preliminary cleaned and merged playback data (Level-0) for downloading via FTP by the POC 24 hours after the end of a pass. A second, final set of Level-0 files will be produced 30 days after reception.

### Data Processing Level

Definitions of SECCHI data processing levels are summarized in Table 3-2.

Table 3-2  Data Processing Level Definition

| Level | Source | Description |
| --- | --- | --- |
| Packets | Spacecraft, MOC | Consultative Committee for Space Data Systems (CCSDS) Packets as transmitted by the spacecraft to the Deep Space Mission System (DSMS) and then the MOC |
| Level-0 | MOC | CCSDS Packet files sorted and duplicates removed; final after 30 days |
| Level-0.5 | POC or DPF | FITS files containing uncompressed (16-bit) images. Values are raw counts (DN). Header contains only telemetry information that came with the image (quick-look) OR all information in telemetry plus any ancillary information necessary to interpret the data (pre-final or final). |
| Level-1 | User Workstation using SolarSoft | FITS files with calibration applied ”on the fly”. Values are physical units (COR, HI) or calibrated DN (EUVI). |
| Level-2 | User Workstation using SolarSoft or DPF | Data products which are a result of combining 2 or more (non-calibration) images. Includes movies, polarized Brightness images, Carrington maps, etc. May or may not be calibrated. |
| Level-3 | User Workstation using SolarSoft | Derived quantities: Electron density, temperature ratios, emission measures, etc. |

”Quick-look” data may be produced from the real-time channel wherever the POC is located (JHU/APL or NRL). Quick-look data will be produced only during commissioning or other times with high real-time allocation. The data product will be FITS files with raw counts (“Level-0.5”); the quick-look Level-0.5 FITS files are differentiated from the final data product by the completeness of the header. The FITS files produced from the real-time channel will be kept indefinitely.

Final SECCHI data will be produced at the NRL DPF. The six (6) time-sorted Level-0 packet files prepared by the MOC will be retrieved and processed daily.Level-0.5 (FITS) images, with all relevant ancillary data in the header, will be produced along with any other SECCHI ancillary data products. After 30 days, these Level-0.5 files will be “Final.”

The "Level-1" data product will be a combination of FITS files and SolarSoft IDL procedures that are executed when reading the file in.

### Data Flow and Data Product Generation

#### Pre-Flight

During instrument development, images will be generated for test and/or calibration purposes. Depending on the stage of development, these files will be produced by the Telescope Development System (TDS) or the integrated SECCHI instrument. The image files will be in Level-0.5 format with header keywords that are relevant to pre-flight. The pre-flight images for all telescopes will be part of the SECCHI data archive at NRL.

#### Flight Operations

Figure 3-1 provides an overview of the different components of the DPS. Data originates at the POC, which in this diagram represents a workstation receiving telemetry from the MOC. This workstation may be located at either JHU/APL or NRL. When at JHU/APL, science and housekeeping data files will be transmitted to NRL via rsync. The three (3) types of data available through the SECCHI POC are the Level-0 (MOC-processed) packet files, real-time or unprocessed packet files, andsocket playback telemetry. The POC will parse the incoming raw telemetry data and will sort the data into image and housekeeeping files. All processed data are archived at NRL.

Figure 3-1  SECCHI Data Processing Flow

#### Beacon Data

The beacon data will follow the same process outlined above up to the Level-0.5 product. The data will be saved as FITS files, with images for display and browsing (byte-scaled) created with the best available background; these display images may be replaced if an the background model is updated. The beacon data will be processed by the STEREO Science Center using the same pipeline as the SECCHI data processing center.

### Data Calibration and Evaluation

The flight science data, including the beacon data, will be compressed using one (1) or more of the onboard compression algorithms. Following the restoration of the original uncompressed image (perhaps with loss of some information), the images will be characterized statistically in the following way:

Noise and standard deviation

Histogram of pixel values

Minimum and maximum pixel values

Average pixel values

The images will also be evaluated to determine the effectiveness of the compression algorithm that was used.

Software procedures will be developed in the IDL to perform the following calibration tasks:

Remove geometric distortion

Locate stars, determine roll angle, and absolute pointing

Remove CCD fixed-pattern noise

Perform photometric calibration

Remove vignetting, stray light, and instrumental polarization

Remove background F-corona from total brightness images to reveal the K-coronal structures

Sharpen resolution using modulation transfer function (TBC)

A variety of on-orbit calibration checks will be performed, using techniques that have been developed and used successfully on data from the Solar and Heliospheric Observatory (SOHO) and Trace missions. Stars and planets will transit through the fields of view of each of the optical systems. Their positions are well known and provide roll angle, absolute pointing, and geometric distortion determinations. Similarly, photometric measurements of stars and planets in transit through the field of view will yield vignetting and photometric calibrations. Instrumental stray light observations can be obtained for the EUVI when a planet transits the field.

Periodic spacecraft rolls will be conducted to permit polarization and stray light calibrations, and periodic offpoints of the spacecraft will permit flat-field calibrations for the EUVI instrument.

Instrument calibration sources (Light-Emitting Diodes [LEDs]) will also be used in flight to check the optical performance of each telescope, and to check the sensitivity of the CCDs.

### Data Distribution and Accessibility

The SECCHI data policy is to have completely open access to all data, including the calibration data and the procedures to calibrate and further process the data. SECCHI images will be available as soon as the routine processing steps have been completed. This is estimated to be within 30 minutes of receipt of the data packets necessary to form an image. After the images are released as Final, the Level 0.5 FITS files will be delivered electronically to the SSC from NRL as available. A Digital Video Disk (DVD) media archive (or whatever medium is the best choice, to be determined closer to launch) will be maintained at NRL. Data will also be delivered electronically to other sites in the U.S. and in Europe. No data will be distributed routinely on hard-copy such as CDROM or DVD.

Browse/display images will be created from the pre-final FITS files using the best available background and will be available on the SECCHI Web server. One (1) copy of each image will be kept as part of the SECCHI archive until replaced by a superior version (if any). The same procedure will be followed for browse movies.The image data will be accessible through the Internet using a searchable database. It will be possible to generate queries using most header keywords as parameters. Temperatures, voltages and other housekeeping parameters can also be obtained through database queries.

IDL procedures and auxiliary data will apply calibration and processing steps as specified by the user. These procedures, calibration files and auxiliary data will be updated as necessary throughout the mission and will be freely available via Internet access as part of the SolarSoft software library (SSW) and database (SSWDB). Community analysis of STEREO observations will be from a virtual center, in that data will be requested from the SSC and/or the NRL DPF and automatically delivered to investigators via the open Internet.

## Data Volume

The decompressed science data is estimated to be about 12 GB per day for both observatories during the prime (two-year) science phase of the mission. Table 3-3 outlines the estimated data volume for all data products, which comes to 12.9 TB for the two-year primary mission.

Table 3-3  SECCHI Data Volume

| Data Product | Bytes/pix | 1kx1k/day/SC | 2-yr Vol. (GB) |
| --- | --- | --- | --- |
| Science images (COR, EUVI) | 2 | 2700 | 8267 |
| Science images (HI) | 4 | 40 | 245 |
| Calibration images | 2 - 4 | ? | 10 |
| Pre-flight images | 2 | NA | 250 |
| Browse images (GIF and JPG) | ~ 0.1 or ~ 0.8 | 2000 | 3062 |
| Browse movies (512x512) | ~ 0.05 | 500 | 38 |
| Science movies (512x512) | 1 | 500 | 766 |
| Ancillary data | varied | ? | 10 |
| 3-D daily model | 2 | 64 | 196 |

## Labeling and Identification

In general, data product files will be named using date and time of observation. Additional characters in the file name will indicate spacecraft, telescope, and level of processing, including whether the data are quick-look data. The file format will be indicated by the suffix. The file format will conform to the following:

yyyymmdd_hhmmssTTSL.typ

S = [a,b,c] for Spacecraft A or B or non-specific

TT = camera: [eu, c1, c2, h1, h2, tk, d[1,2…]] for EUVI, COR1, COR2, HI1, HI2, Talktronics, SECCHI camera development model [1,2,…] or other characters TBD to represent other (preflight) cameras

L = p for pre-flight images

L = r for Level 0.5 real-time (Quick-look) flight images

L = 0 for Level 0.5 Middle or Final flight images

L = [1, 2, …] for flight images at level 1, 2 etc.

Yyyymmdd_hhmmss = year, month, day and hour, minute and second of the observation time

Typ = suffix indicating format, such as fts, gif, jpg, txt, ….

## Standards Used in Generating Data Products

### FITS Standard

The SECCHI image files will conform to the FITS standard as specified in Table 2-1 and clarifications may apply.

### Time Standard

Time is Universal Time (UTC) unless otherwise stated. According the Flight Software Requirements document, “The exposure start time of all pictures shall be derivable by ground processing to Universal Time with an accuracy of 0.5 second.”

### Coordinate Systems

The proposed coordinate system for SECCHI data is Helioprojective Cartesian using Gnomic projection. “Helioprojective Cartesian” indicates heliocentric coordinates where physical distances are replaced with angles, in recognition that observations are projected against the celestial sphere. It is an observer-centric system. The gnomic projection, or TAN, comes into play because the image is focused onto a flat focal plane, in this case a CCD detector (See Thompson, 2000, in Appendix A, Section A.2.).

# Data Analysis

All Co-investigators may contribute to any aspect of the data analysis effort. Various groups have been established with bulletin boards to facilitate the communication between the groups. Each group has a leader or moderator. While cross-institutional collaborations are encouraged, most efforts at this time are based within a single institution.

At this time the various analysis groups and their moderators are:

3-D Reconstruction and Visualization:	John Cook <cook@louis14.nrl.navy.mil>

CME Science: 			Ken Dere <dere@halcyon.nrl.navy.mil>

Space Weather:			David Webb <David.Webb@hanscom.af.mil>

MHD Modeling			Jim Klimchuk <jklimchuk@ssd5.nrl.navy.mil>

# Data Processing System Development Plan

## Timeline

Image Decompression			3/19/04

Processing Pipeline from TLM to FITS	6/24/04

Database				8/1/05

Website				8/1/05

Data Archive			10/1/05

Order Archive Systems			5/15/05

STEREO Analysis			11/15/05

CME Search and Characterization		11/15/05

Generate Movies			11/15/05

Geometric & Photometric Calibration	11/15/05

Process to Level 1			11/15/05

## Software Reuse Strategy

Much of the image processing (decompression, FITS format, movies, etc.) is similar if not identical to that done for the Large Angle Spectrometric COronagraph (LASCO) and the Extreme-ultraviolet Imaging Telescope (EIT) on SOHO. The basic SECCHI image processing software will use the same IDL procedures as LASCO with slight modifications. For the TDS freely available C libraries exist to read/write FITS files (CFITSIO).

## Testing

The DPS will be tested during STEREO Integration and Test (I&T). Observing plans for post-launch verification of instrument calibration will be developed before launch.

## Configuration Management and Backup Plan

### Software

Configuration management (CM) of data processing procedures will be done with the Concurrent Versions System (CVS). Calibration data will also be under CM. Information on calibration revision level will be contained in image headers, which are the output of calibration software.

Besides the ability to restore previous versions of software using SCCS, backups of software will exist as multiple copies in the SSW and on regular tape backups. The SECCHI library of data processing procedures will be on a shared disk, so processing may be done on any computer in the network.

### Data

There will be at least three (3) copies of the processed level 0.5 FITS images and ancillary data products:

1. The primary archive online at NRL

[2. On removable media (such as DVD) at NRL]??

3. At the SSC

There will be one (1) complete set of all SECCHI raw telemetry (science and housekeeping) in the SSC archive. This archive is replicated at NRL.

## Equipment and Space Requirements

Table 5-1  Equipment and Space Requirements

| Use | Equipment | Need Date |
| --- | --- | --- |
| Dedicated Web server | 1 Sparc | Aug. 2005 |
| Data Processing (mission sims) | 2 Sparc | April. 2004 |
| Data Processing (flight ops) | 2 Sparc | Aug. 2005 |
| Database | 1 Sparc | Aug. 2005 |
| Archive | 2 DVD writers and 13 TB of storage for 2 years: DVDRAM jukeboxes or SAN solution | Aug. 2005 |
| Data Distribution | 2 Sparc | Sept. 2005 |
| Generate movies | 3 Sparc | Nov. 2005 |
| Displays | Two 22”CRT, 8 17” LCD, plus servers | Jan. 2006 |

DVDRAM		Digital Video Disk Random Access Memory		SAN	Storage Area Network

CRT		Cathode Ray Tube					LCD	Liquid Crystal Display

# Acronym List

| Acronym | Definition |
| --- | --- |
| ADC | Analog to digital converter |
| Al | Aluminum |
| ApID | Application Identifier |
| APL | The Johns Hopkins University Applied Physics Laboratory |
| AR | Anti-Reflective |
| B | Brightness |
| CCD | Charge Coupled Device ((detector) |
| CCSDS | Consultative Committee for Space Data Systems |
| CDROM | Compact Disk Read-Only Memory |
| CEB | ((SECCHI) Camera Electronics Box |
| CFITSIO | A FITS File Subroutine Library |
| CM | Configuration Management |
| CME | Coronal Mass Ejection |
| COR | SECCHI Coronagraph |
| CRT | Cathode Ray Tube ((monitor) |
| DBMS | Database Management System |
| DN | Digital Number ((photon counts) |
| DPF | Data Processing Facility |
| DPS | Data Processing System |
| DSMS | Deep Space Mission System ((= DSN) |
| DSN | Deep Space Network |
| DVD | Digital Video Disk |
| DVDRAM | Digital Video Disk Random Access Memory |
| EIT | Extreme-ultraviolet Imaging Telescope on SOHO |
| EUV | Extreme-UltraViolet |
| EUVI | Extreme-UltraViolet Imager |
| FITS | Flexible Image Transport System |
| FPS | EUVI Fine Pointing System |
| FSW | ((SECCHI) Flight Software |
| FTP | File Transfer Protocol |
| GB | Gigabyte ((1 billion bytes) |
| GIF | Graphics Interchange Format |
| GSFC | Goddard Space Flight Center |
| GT | ((SECCHI) Guide Telescope |
| HI | ((SECCHI) Heliospheric Imager ((also refers to the HI package CEB) |
| I&T | Integration and Test |
| ICD | Interface Control Document |
| IDL | Interactive Data Language |
| JHU/APL | The Johns Hopkins University Applied Physics Laboratory |
| JPEG, JPG | Joint Photographic Experts Group ((glossy image compression) |
| LASCO | Large Angle Spectrometric COronagraph on SOHO |
| LCD | Liquid Crystal Display |
| LED | Light Emitting Diode |
| LMSAL | Lockheed Martin Solar and Astrophysics Laboratory |
| LZ | Level 0 ((data) |
| MHD | Magnetohydrodynamic |
| MOC | ((STEREO) Mission Operations Center |
| MPEG, MPG | Motion Picture Exports Group |
| MVI | NRL-developed IDL movie format |
| NA | Not Applicable |
| NASA | National Aeronautics and Space Administration |
| NOST | NASA Office of Standards and Technology |
| NRL | U.S. Naval Research Laboratory |
| PB | Polarized Brightness |
| POC | Payload Operations Center |
| RAL | Rutherford Appleton Laboratory |
| S/C or SC | Spacecraft |
| SAN | Storage Area Network |
| SCCS | Source Code Control System |
| SCIP | Sun Centered Imaging Package ((includes SECCHI COR1, COR2, EUVI) |
| SEB | SECCHI Electronics Box |
| SECCHI | Sun Earth Connection Coronal and Heliospheric Investigation |
| SOHO | Solar and Heliospheric Observatory |
| SSC | STEREO Science Center |
| SSC | STEREO Science Center |
| SSW | SolarSoft IDL Libraries |
| SSWDB | SolarSoft Databases |
| STEREO | Solar TErrestrial RElations Observatory |
| TAN | Tangent |
| TB | Terabyte ((1 trillion bytes) |
| TBC | To be confirmed |
| TBD | To be determined |
| TDS | Telescope Development System |
| TLM | Telemetry |
| UNIX | X/Open operating system |
| UTC | Universal Time |
| WWW | World Wide Web |

Appendix A	DEFINITION OF SECCHI Level 0.5 FITS HEADER

As of October 22, 2002.

This appendix exists as a separate document which may be updated separately.

A.1	Overview

A.1.1	Main Header

The items in the box are part of the pre-flight image header. Each group of keywords is to be added as they become applicable.

- Minimum Header: All images taken with SECCHI cameras should have this header information, from camera level testing onward.

- Preflight Only: Only images taken before launch will have these keywords.

- Misc. Camera/CCD values: Values specific to CCD and camera characteristics. Should be in all images from camera level testing onward.

- Used from telescope level testing onward: These keywords are applicable only if mechanisms apart from the camera are used in taking an exposure.

- Housekeeping Parameters: Ancillary information indirectly related to an image.

- Software-Dependent Values: These values are dependent on on-board image processing, nominally the SECCHI Flight Software (FSW).

- Computed from information external to the image, on the ground: These values have ancillary information about spacecraft position, attitude, etc. This includes coordinate system definition.

- Computed from image values, on the ground: Values computed from the image but not in the FSW are included here.

- History:  Examples of history field values.

A.1.2	SECCHI FITS Extension

Information about individual exposures used to compute a single image from a sequence is contained in an ASCII table extension to the FITS header.

- Extension Table Column (Field) Definitions: These are the values that will be recorded for each exposure.

- Keywords for FITS Extension: Each column in a FITS extension has its own set of keywords to define the type of value.

A.1.3	Table Description

The following tables have four (4) columns: KEYWORD, TYPE, VALUES, and DESCRIPTION.

KEYWORD gives the name of the FITS keyword and may be up to eight (8) characters.

TYPE refers to the data type of the header value:

S	String

I	Integer

R	Real

L	Logical

The size of the data depends upon the data type. For example S*2 is a two (2) character string, whereas I*2 is a two (2) byte integer (16 bits).

VALUES shows the range of values that the KEYWORD can take.

DESCRIPTION gives a short description of the keyword. At the end of the description is a reference to a FSW requirement, if any. (NOTE: FSW requirement numbers not up-to-date as of 9/10/02.)

A.2	References

"Coordinate Systems for Solar Image Data", http://orpheus.nascom.nasa.gov/~thompson/papers/coordinates.ps

"Definition of the Flexible Image Transport System (FITS)", http://archive.stsci.edu/fits/fits_standard/

"Definition of LASCO Level 1 FITS Header Keywords", http://lasco-www.nrl.navy.mil/level_1/level_1_keywords.html

"SSW Keyword/Tag Definitions", http://www.lmsal.com/solarsoft/ssw_standards.html

"A User's Guide for the Flexible Image Transport System (FITS)", http://fits.gsfc.nasa.gov/documents.html#Uguide

Detailed proposal for representing world coordinates in FITS (http://www.aoc.nrao.edu/~egreisen/inFITS.html):

Representations of world coordinates in FITS by Greisen and Calabretta, 31-December-2001.

Representations of celestial coordinates in FITS by Calabretta and Greisen, 12-December-2001.

Representations of spectral coordinates in FITS by Greisen and Valdes, 31-December-2001

SOHO object list http://Orpheus.nascom.nasa.gov/object.dat

A.3	Main Header

| Keyword | Type | Values | Description |
| --- | --- | --- | --- |
|  |  |  | Minimum Header |
| SIMPLE | L | T | Conforms to FITS standard |
| BITPIX | I*2 | 16,32 | Number of bits per pixel |
| NAXIS | I*2 | 0,2 | Number of axes in the image (0 indicates header only) |
| NAXIS1 | I*2 | Positive | Length of the first axis (columns,x) |
| NAXIS2 | I*2 | Positive | Length of the second axis (rows,y) |
| DATE | S*23 | Any | Date of file generation, in CCSDS standard format (UTC): "1996-05-21T17:28:48.208" |
| FILENAME | S*23 | --> | Name of the FITS file: yyyymmdd_hhmmssTTSL.fts Format as follows: S = Spacecraft (a,b,c)(c is for anything that is not associated with one or the other s/c); TT = a string representing telescope or camera: eu=EUVI, c1=COR1, c2=COR2, h1=HI1, h2=HI2, gt = GT; L = a digit representing processing level, or ‘r’ for quick-look or ‘p’ for pre-flight The rest is year, month, day, hour, minute, second (equivalent to DATE-OBS) |
| FILEORIG | S*17 | Any | Name of the raw telemetry file in the format YYMMDD_HHMMSS[a,b].img. The date and time are that of the first packet of the image; a or b indicates spacecraft. |
| DATE-OBS | S*23 | Any | Date and time of the start of the (first) exposure (UTC): 2006-05-20t00:40:05.407 (accuracy level of time known from HISTORY) |
| EXPTIME | R*4 | Any | Duration of the exposure (seconds); if > 1 exposure, then the sum (individual exptimes in header extension) (FSW 410, 423) |
| SUMCCD | I*2 | 1,2,4 | Number of rows and columns being summed on the CCD (FSW 431) |
| P1(2)COL | I*2 | 1..? | CCD column number of start(end) of image; 1-?? are underscan pixels, ??-???? are imaging pixels, ???? - ????? are overscan pixels (FSW 212,431) (NOTE: First column is 1, not 0.) |
| P1(2)ROW | I*2 | 1..? | CCD row number of start(end) of image; 1-???? are imaging rows, ????-????? are overscan rows (FSW 212,431) |
| INSTRUME | S*8 | SECCHI | Name of the instrument |
| OBS_ID | I*2 | 0..32767 | ?? Observing Sequence ID (number): A number that specifies an instrument setup/configuration or sequence of exposures (such as polarizer sequence); can be used to search the database for the same types of images. Corresponds with Observation ID in Planning Tool. (FSW 050) - Use to indicate test configuration, together with COMMENT or HISTORY? - What about campaign ID? |
| VERSION | S*6 | Yymmdd | ?? Version number of header (carry from camera testing through flight) (same as task version number, FSW 050) |
| ORIGIN | S*8 | NRL GSFC UBHAM LMSAL APL ... | Institution where FITS file was created |
| BUNIT | S*20 | DN DN/s UNITLESS MSB etc. | Physical unit of array values (after BZERO and BSCALE, if present, are applied) |
| BLANK | I*1 | 0 | Value of missing or masked data. |
| COMMENT | S*80 | Any | Comments. Can be repeated |
| COMMENT | S*80 | Any | 'FITS coordinate for center of 1024x1024 image is (512.5,512.5).' |
| HISTORY | S*80 | Any | History. Can be repeated. |
| END |  |  | Last keyword in the FITS header |
|  |  |  | Pre-flight only |
| OBSERVER | S*20 | Any | Character string identifying who acquired the data associated with the header |
| OBJECT | S*20 | ? | Object observed; maintain constantly updated list of configurations which will be displayed in a menu? |
| COMMENT | S*80 | Any | Observer will have ability to input comments into FITS header |
|  |  |  | Camera/CCD values |
| EXPDELAY | R*4 | Any | Measured exposure delay time (seconds) (FSW ???) |
| EXPCMD | R*4 | Any | ???Commanded exposure delay time (seconds) (FSW ???) |
| EXPCLR | R*4 | Any | Length of time since CCD clear (seconds) (FSW ???) |
| EXPOPEN | R*4 | Any | Length of time to open shutter (seconds) (FSW ???) |
| EXPCLOSE | R*4 | Any | Length of time to close shutter (seconds) (FSW ???) |
| EXPOUT | R*4 | Any | Length of time, shutter close to camera readout (seconds) (FSW ???) |
| OFFSET | I*2 | Any | Electronic offset in DN; computed on ground |
| VIDGAIN | I*2 | Any | Video gain (FSW 431?); computed on ground |
| DITHER | L | T(F) | Dithering readout mode is on(off) |
| READPORT | S*1 | A,B | CCD readout port (FSW 411,431) |
| MODE | S*8 | DUMP INTEGRAT READOUT CONT | CCD camera mode (FSW 434)? |
| CCD_WFH | S*? | List of numbers | Row numbers (from reference table) that are in the camera wave function table for horizontal readout |
| CCD_WFV | S*? | List of numbers | “ vertical readout |
| TEMP_CCD | R*4 | Any | Temperature of the CCD (degrees C) |
|  |  |  | Used from telescope level testing onward |
| OBSRVTRY | S*8 | STEREO[AB] | Name of the satellite. (Replaces TELESCOP keyword.) |
| DETECTOR | S*8 | EUVI COR1 COR2 HI1 HI2 | Name of the telescope within SECCHI |
| FILTER | S*8 | Clear Al+1 | Position of the EUVI filter (FSW 410,411,442) |
| POLAR | I*2 | 0..? | Position of the polarizer, degrees from vertical WRT to CCD “North,” rounded to nearest integer; if the image is computed from a sequence, then this is the sum of the positions during the sequence (FSW 410,411,442) (Polarizer steps in increments of 2.5 °, or 144 positions.) |
| SHUTTER | L | T(F) | Shutter was (not) commanded open during the exposure (FSW 411,424?,.442?) |
| SECTOR | I*2 | 171 195 284 304 | Sector (wavelength in Angstroms) of EUVI exposure (FSW 411,424?,442) |
| SHUTTDIR | S*3 | CW CCW | Direction of motion of the shutter from the CCD's POV (FSW 424?,442?) |
| LAMP | L | T(F) | Calibration lamp(s) was (not) commanded on. Specific Lamp configuration specified in IP_PROG or OBS_PROG or OBS_ID. (FSW 411,424?) |
| DOOR | L | T(F) | Telescope door was open (closed) (FSW 411?,424?,442) |
|  |  |  | Housekeeping parameters |
| TEMP1(23) | R*4 | Any | Temperatures, degrees C. Include for pre-flight AND flight. (FSW 151,424?,435) |
|  |  |  | Software-dependent values: Use with FSW |
| EXTEND | L | T | Indicates that there may be an extension. Does not necessarily mean an extension is present. |
| SEBX(Y)SUM | I*2 | 1 2 4 8 16 | Number of columns(rows) being summed in the SECCHI Electronics Box (FSW ???) |
| COMPRSSN | S*8 | NONE RICE WAVELET ... | Code indicating the algorithm used in compressing the data (FSW 215,410) (Could include compression factor as part of the string.) |
| DATE_MID | S*23 | Any | Date of midpoint of the exposure(s) (UTC standard) |
| OBT_TIME | R*4 | Any | Value of the SECCHI On-Board Time (seconds) (FSW 043) |
| OBS_PROG | S*8 | Normal, Cal Lamp, Dark, LineScan, PolSeq ... | Description of the Observing Program which generated the image. (Equivalent to LEB_PROG on LASCO) (FSW 217,410,411,416) - Relation to OBS_ID? |
| IP_PROG | S*8 | B, PB, %P, Sum, Diff, Binning ... | Description of the onboard Image Processing routine which produced the image, usually from several exposures. - Relations to OBS_ID? |
| IMGCTR | I*2 | Any | Sequential counter since: the last SEB reboot? or otherwise reset? Per telescope? Per CEB? (FSW 240?) |
| IMGSEQ | I*2 | 0..32767 | Number of the image in the current sequence, starting at 0 (FSW 240?) |
| RECTIFY | L | T(F) | Status of rectification to put solar north to the top of the image |
| R1(2)COL | I*2 | Any | The rectified begin(end) X-coordinate, as though rectification had been unnecessary. If RECTIFY is F, then this is equal to P1(2)COL. |
| R1(2)ROW | I*2 | Any | Rectified P1(2)ROW |
| SYNC | L | T(F) | The image is (not) commanded to be synchronous with the other spacecraft. |
| JITTER | R*4 | Any | Mean amplitude of jitter during exposure(s) (Arcseconds) (Computed onboard from GT values) (FSW 218,311,322) |
| JITRSDEV | R*4 | Any | Standard deviation of JITTER, computed onboard. |
| FPS_ON | L | T(F) | EUVI fine pointing system (FPS) is (not) activated during exposure(s) (FSW 320,424?) |
| SCFP_ON | L | T(F) | Fine pointing bit from spacecraft is (not) activated. (FSW 322) |
| SCANT_ON | L | T(F) | The “move antenna” bit from the spacecraft is (not) set. |
| CADENCE | R*4 | Any | Number of seconds between exposures/sequences for the current observing program (not individual exposures in a sequence). Is zero if not part of a repeating observing sequence. (FSW 410?) |
| FLARE | L | T(F) | A flare event has (not) been triggered by the flare detection algorithm prior to or during this observation sequence. (FSW 413,424?) |
| FCOUNT | I*4 | Any | Count level used by the flare detection algorithm to set FLARE on (FSW 413,424?) |
| FROW | I*2 | Any | X-coordinate of FCOUNT (FSW ???) |
| FCOL | I*2 | Any | Y-coordinate of FCOUNT (FSW ???) |
| S1(2)COL | I*2 | Any | Start (end) X-coordinates of sub-image extracted by the FSW, equivalent to P1(2)COL (FSW 416) |
| S1(2)ROW | I*2 | Any | Start (end) Y-coordinates (FSW 416) |
| COSMICS | I*4 | Any | Number of pixels removed from image by cosmic ray removal algorithm (if image is from a sequence, then the mean) (FSW 217,411,416) |
| N_IMAGES | I*2 | 0..1000+ | Number of CCD readouts used to compute the image (Number of extension headers = N_IMAGES –1) |
| VCHANNEL | I*2 | 6 7 ? | Virtual channel of telemetry downlink (7=Realtime, 6=Playback, ?=Beacon) (FSW 410) |
| MASK | S*? | 0..? | Space-delimited list of coordinates of pixel blocks masked by the flight software (FSW 417) |
| CME | L | T(F) | CME detection has (not) been triggered. (FSW 217,424?) |
|  |  |  | Computed from information external to the image, on the ground |
| SOURCE | S*2 | RT, LZ | Real-time or Level Zero |
| RSUN | R*4 | Any | Radius of sun (Arcseconds) |
| CROTA | R*4 | Any | Rotation angle of image about axis perpendicular to the plane of the image. Specified in degrees CCW relative to the Y direction. (Obsolete) (Sign is opposite that of correction.) |
| CRPIXi | R*4 | Any | The pixel coordinates of disk center, even if that’s outside the array. |
| CDi_j | R*4 | Any | A coordinate transformation matrix; platescale and rotation information are included in these keywords (replaces CDELTi and CROTAi) |
| CRVALj | R*4 | Any | The reference data coordinates corresponding to CRPIX1(2). For example, if the pixel coordinates specify the origin, then set CRVAL1 and CRVAL2 to zero. |
| CTYPE1j | S*8 | HPLN-TAN | A string value representing the type of each coordinate axis. TBD Helioprojective Gnomic (TAN) Projection (PROPOSED) CTYPE1 is for x (westward angle) axis ((x). |
| CTYPE2 | S*8 | HPLT-TAN | Helioprojective Gnomic Projection for y (northward angle) axis ((y). (PROPOSED) |
| CUNITj | S*8 | Arcsec | The units of the coordinates along axis j. |
| CDELTj | R*8 | Any | The width and height of a pixel in data units, where units are specified by CUNITj (Same as PLATESCL) (Obsolete) |
| X(Y)CEN | R*4 | Any | East-West (North-South) FOV center of image relative to sun center in CDELT1(2) units, positive West (North). X(Y)CEN is related to the above FITS keywords by: X(Y)CEN = CRVAL1(2) + CDELT1(2) * [(NAXIS1(2)+1)/2 - CRPIX1(2)] (units = arcseconds) |
| ---X_OBS | R*8 | Any | Position of spacecraft in x direction (meters). Coordinate system TBD. (See paper by Thompson in references.) |
| ---Y_OBS | R*8 | Any | “ in y direction “ |
| ---Z_OBS | R*8 | Any | “ in z direction “ |
| LONPOLE | I*1 | 180 | Degrees (default for helioprojective coordinates) |

A.3.1	Coordinate System

Factors/requirements in selection of coordinate system:

Easily correct for B angle

Identify central meridian

Easily correct for differences in solar radius from distance

Ecliptic

Ascertain position relative to planets

Possibilities suggested so far:

EIT uses heliocentric ecliptic

Helioprojective Cartesian with TAN projection

RA and DEC with TAN projection

| Keyword | Type | Values | Description |
| --- | --- | --- | --- |
| MJD_OBS | R*8 | Any | Beginning of observation (Julian Day (seconds) – 2400000.5) |
| EAR_TIME | R*4 | Any | Time(Sun to Earth) - Time(Sun to S/C) (Seconds) |
| SUN_TIME | R*4 | Negative | Time(Light-travel time from Sun to S/C.) (Seconds) |
| CMDOFFSE | R*4 | Any | Commanded offset from schedule (Seconds) (Exact definition TBD) |
| CRPIX1(2) | R*4 | Any | Column(Row) number of the reference pixel, which is sun center. May be computed from GT data in telemetry? (FSW 218,311,322) |
| ANTENNA | S*12 | Any | Antenna which received (most) of the packets for this image |
| OBJECT | S*20 | ? | Type of object observed; maintain constantly updated list of features which will be displayed in a menu? See ref 7 above |
| OBJECTID | I*2 | Any | Active region number |
|  |  |  | Computed from image values, on the ground |
| DATAMIN | R*4 | Any | Minimum value of the image, including the bias |
| DATAMAX | R*4 | Any | Maximum value of the image |
| DATAZER | I*4 | Any | Number of zero pixels in the image |
| DATASAT | I*4 | Any | Number of saturated values in the image |
| DSATVAL | R*4 | Any | Value used as saturated |
| DATAAVG | R*4 | Any | Average value of the image |
| DATASIG | R*4 | Any | Standard deviation in computing the average |
| DATAP01 | I*4 | Any | Intensity of 1st percentile of image |
| DATAP10 | I*4 | Any | Intensity of 10th percentile image |
| DATAP25 | I*4 | Any | Intensity of 25th percentile of image |
| DATAP75 | I*4 | Any | Intensity of 75th percentile of image |
| DATAP90 | I*4 | Any | Intensity of 90th percentile of image |
| DATAP95 | I*4 | Any | Intensity of 95th percentile of image |
| DATAP98 | I*4 | Any | Intensity of 98th percentile of image |
| DATAP99 | I*4 | Any | Intensity of 99th percentile of image |
| MISSLIST | S*80 | Any | Space-delimited list of missing blocks. The numbers are the 1D subscripts of a 32x32 array representing superpixels of the array. |
| NMISSING | I*4 | Any | Number of missing blocks (not including on-board masked regions) |
| BSCALE | R*8 | Any | If missing, then assumed to be 1: output data = FITS data * BSCALE + BZERO |
| BZERO | R*8 | Any | If missing, then assumed to be zero |
|  |  |  | HISTORY: (Examples from LASCO, just to give an idea....) |
| HISTORY |  |  | 'Vxx dd mmm yyyy reduce_level_1,'d2nnnnnn.fts','d5nnnnnn.fts'' |
| HISTORY |  |  | 'Vxx dd mmm yyyy get_exp_factor, old_exp_time, bias' |
| HISTORY |  |  | 'Vxx dd mmm yyyy vigfilename.fts' |

A.4	SECCHI FITS Extension

Information about individual exposures used to compute a single image from a sequence is contained in an ASCII table extension to the FITS header. With the exception of DELTTIME, the values in the columns (fields) have the same meaning as the corresponding keywords in the main header, if the main header is for a single image. If an image consists of a single exposure, this table is optional and would have a single row. There is one row for each exposure, including the first one in the sequence.

A.4.1	Extension Table Column (Field) Definitions

| Field | Heading | Values | Description |
| --- | --- | --- | --- |
| 1 | DELTTIME | Any | Time from DATE-OBS (seconds) of the beginning of the (first) exposure. First row is always zero. |
| 2 | EXPTIME | Any | Duration of the exposure (seconds) |
| 3 | SUMROW | 1,2,4 | Number of rows being summed on the CCD (FSW 433) |
| 4 | SUMCOL | 1,2,4 | Number of columns being summed on the CCD (FSW 433) |
| 5 | POLAR | 0..179 | Position of the polarizer, degrees from vertical WRT to detector |
| 6 | SHUTTR | T(F) | Shutter was (not) commanded open during the exposure |
| 7 | APRT_SEL | T(F) | Aperture selector was (not) commanded open (COR1 only) |
| 8 | SHUTTDIR | CW CCW | Direction of motion of the shutter from the CCD's POV (FSW ?) |
| 9 | LAMP | T(F) | Calibration lamp was (not) commanded on (FSW 411) |
| 10 | DOOR | T(F) | Telescope door was open (closed) |
| 11 | IMGCTR | Any | Sequential counter since the last SEB reboot |
| 12 | IMGSEQ | Any | Number of the image in the current sequence, starting at 0 |
| 13 | ASYNCH | T(F) | Flight software is (not) in asynchronous mode (FSW 020,419?) |
| 14 | FLARE | T(F) | A proton event has (not) been triggered by the flare detection algorithm prior to this exposure (FSW 413) |
| 15 | FCOUNT | Any | Count level used by the flare detection algorithm to detect proton event (FSW 413) |
| 16 | FROW | Any | X-coordinate of FLEVEL (FSW ???) |
| 17 | FCOL | Any | Y-coordinate of FLEVEL (FSW ???) |
| 18 | COSMICS | Any | Number of pixels removed from image by cosmic ray removal algorithm (FSW 217,411) |

The following illustrates the layout of each row in the extension table:

00000000011111111112222222222333333333344444444445555555555666666666677777777778

12345678901234567890123456789012345678901234567890123456789012345678901234567890

rrr.rrr rrr.rrr ii ii iii l l sss l l iiii iiii l l iiiiii iiii iiii iiiiii

A.4.2	Keywords for FITS Extension

| Keyword | Type | Values | Description |
| --- | --- | --- | --- |
| XTENSION | S*8 | TABLE | Required |
| BITPIX | I*2 | 8 | Indicates printable ASCII characters |
| NAXIS | I*2 | 2 | Axes are the rows and columns of the table |
| NAXIS1 | I*2 | 74 | Number of characters in a table row |
| NAXIS2 | I*2 | Any | Number of exposures in the sequence (=NUM_EXP) |
| PCOUNT | I*2 | 0 | Required |
| GCOUNT | I*2 | 1 | Required |
| TFIELDS | I*2 | 18 | Number of fields in each table row |
| TBCOL1 | I*2 | 1 | Column number of first character in first field |
| TFORM1 | S*4 | F7.3 | FORTRAN format of field 1: single precision floating point |
| TTYPE1 | S*8 | DELTTIME | Heading for field 1. |
| TUNIT1 | S*7 | Seconds | Units of field 1. |
| TBCOL2 | I*2 | 9 | Column number of first character in field 2 |
| TFORM2 | S*4 | F7.3 | FORTRAN format of field 2: single precision floating point |
| TTYPE2 | S*7 | EXPTIME | Heading for field 2. |
| TUNIT2 | S*7 | Seconds | Units of field 2. |
| TBCOL3 | I*2 | 17 | Column number of first character in field 3 |
| TFORM3 | S*2 | I2 | FORTRAN format of field 3: integer |
| TTYPE3 | S*6 | SUMROW | Heading for field 3. |
| TUNIT3 | S*2 | NA | Units of field 3. |
| TBCOL4 | I*2 | 20 | Column number of first character in field 4 |
| TFORM4 | S*2 | I2 | FORTRAN format of field 4: integer |
| TTYPE4 | S*6 | SUMCOL | Heading for field 4. |
| TUNIT4 | S*2 | NA | Units of field 4. |
| TBCOL5 | I*2 | 23 | Column number of first character in field 5 |
| TFORM5 | S*2 | I3 | FORTRAN format of field 5: integer |
| TTYPE5 | S*8 | POLAR | Heading for field 5. |
| TUNIT5 | S*7 | Degrees | Units of field 5. |
| TBCOL6 | I*2 | 27 | Column number of first character in field 6 |
| TFORM6 | S*2 | A1 | FORTRAN format of field 6: character |
| TTYPE6 | S*6 | SHUTTR | Heading for field 6. |
| TUNIT6 | S*7 | Logical | Units of field 6. |
| TBCOL7 | I*2 | 29 | Column number of first character in field 7 |
| TFORM7 | S*2 | A1 | FORTRAN format of field 7: character |
| TTYPE7 | S*8 | APRT_SEL | Heading for field 7. |
| TUNIT7 | S*7 | Logical | Units of field 7. |
| TBCOL8 | I*2 | 31 | Column number of first character in field 8 |
| TFORM8 | S*2 | A3 | FORTRAN format of field 8: character |
| TTYPE8 | S*8 | SHUTTDIR | Heading for field 8. |
| TUNIT8 | S*8 | Dirction | Units of field 8. |
| TBCOL9 | I*2 | 35 | Column number of first character in field 9 |
| TFORM9 | S*2 | A1 | FORTRAN format of field 9: character |
| TTYPE9 | S*4 | LAMP | Heading for field 9. |
| TUNIT9 | S*7 | Logical | Units of field 9. |
| TBCOL10 | I*2 | 37 | Column number of first character in field 10 |
| TFORM10 | S*2 | A1 | FORTRAN format of field 10: character |
| TTYPE10 | S*4 | DOOR | Heading for field 10. |
| TUNIT10 | S*7 | Logical | Units of field 10. |
| TBCOL11 | I*2 | 39 | Column number of first character in field 11 |
| TFORM11 | S*2 | I4 | FORTRAN format of field 11: integer |
| TTYPE11 | S*6 | IMGCTR | Heading for field 11. |
| TUNIT11 | S*4 | None | Units of field 11. |
| TBCOL12 | I*2 | 44 | Column number of first character in field 12 |
| TFORM12 | S*2 | I4 | FORTRAN format of field 12: integer |
| TTYPE12 | S*6 | IMGSEQ | Heading for field 12. |
| TUNIT12 | S*4 | None | Units of field 12. |
| TBCOL13 | I*2 | 49 | Column number of first character in field 13 |
| TFORM13 | S*2 | A1 | FORTRAN format of field 13: character |
| TTYPE13 | S*4 | ASYNCH | Heading for field 13. |
| TUNIT13 | S*7 | Logical | Units of field 13. |
| TBCOL14 | I*2 | 51 | Column number of first character in field 14 |
| TFORM14 | S*2 | A1 | FORTRAN format of field 14: character |
| TTYPE14 | S*4 | FLARE | Heading for field 14. |
| TUNIT14 | S*7 | Logical | Units of field 14. |
| TBCOL15 | I*2 | 53 | Column number of first character in field 15 |
| TFORM15 | S*2 | I6 | FORTRAN format of field 15: integer |
| TTYPE15 | S*6 | FCOUNT | Heading for field 15. |
| TUNIT15 | S*6 | Counts | Units of field 15. |
| TBCOL16 | I*2 | 60 | Column number of first character in field 16 |
| TFORM16 | S*2 | I4 | FORTRAN format of field 16: integer |
| TTYPE16 | S*4 | FROW | Heading for field 16. |
| TUNIT16 | S*3 | Row | Units of field 16. |
| TBCOL17 | I*2 | 65 | Column number of first character in field 17 |
| TFORM17 | S*2 | I4 | FORTRAN format of field 17: integer |
| TTYPE17 | S*6 | FCOL | Heading for field 17. |
| TUNIT17 | S*6 | Column | Units of field 17. |
| TBCOL18 | I*2 | 70 | Column number of first character in field 18 |
| TFORM18 | S*2 | I6 | FORTRAN format of field 18: integer |
| TTYPE18 | S*6 | COSMICS | Heading for field 18. |
| TUNIT18 | S*6 | Pixels | Units of field 18. |